## Slide 1: DHCP and Router Advertisement Options for Encrypted DNS Discovery
https://tools.ietf.org/html/draft-ietf-add-dnr
March 2021
M. Boucadair (Orange)
T. Reddy (McAfee)
D. Wing (Citrix)
N. Cook (Open-Xchange)
Tommy Jensen (Microsoft)

## Slide 2: Active Issues
https://github.com/ietf-wg-add/draft-ietf-add-dnr/issues (3 open)
  Source xml, but will prepare a source md file soon
Will focus on this issue:
"Most of the draft seems to concern the exact formats of how to deliver resolver information over DHCP/RA, and I think these formats should largely be rewritten to harmonize with DEER.” (Ben Schwarz)

## Slide 3: Which Information is Discovered?
Return the minimal information to establish an authenticated connection with a DNS resolver
Two options are defined
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| OPTION_V6_DNR_ADN | Option-length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Enc DNS Flags | |
+---------------+ +
| |
~ authentication-domain-name ~
| |
+---------------------------------------------------------------+
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| OPTION_V6_DNR_ADD | Option-length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Enc DNS Flags | Unassigned | Port Number |
+---------------+---------------+-------------------------------+
| |
| ipv6-address |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| ipv6-address |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ... |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Follows
Follow the guidelines in RFC7272

## Slide 4: Relationship with DDR
"Upon discovery of a DoH resolver (Sections 4, 5, and 6), the DoH client may contact that DoH resolver to retrieve the list of supported DoH services using DDR [I-D.ietf-add-ddr]. This will allow the client to discover the resolver's supported DoH templates or DoH resolvers that the discovered resolver designates using DNS SVCB queries [I-D.schwartz-svcb-dns]. The designated DoH resolvers and DoH resolver discovered using DHCP/RA may be hosted on the same or distinct IP addresses." (Excerpt from draft-ietf-add-dnr)

## Slide 5: Why Defining Two Options?
The initial design in 05/20 proposed the ADN option only while the address is conveyed in the legacy Do53 @ List
That design was abandoned because it was suboptimal:
  It requires probing if the designated encrypted DNS services are not available on the same IP address(es)
  It requires falling back to Do53 to discover the IP addresses and the alternate port number

## Slide 6: Issue: Harmonize Information with DDR
What additional information do we need to convey in the options?
  URI Templates?
  Other information?

## Slide 7: Issue: URI Templates in RA/DHCP?
Why?
  Provide a customized DNS configuration within a local network
There are trade-offs
  Some issues
    May increase the size of RA/DHCP messages
  Some advantages
    Clients can immediately use the service(s); no need for extra queries to retrieve the URIs
    Does not interfere with DNS exchanges to “customize” the available services
    SVCB DNS does not mandate DNSSEC and the Do53 response can be modified by an attacker
    RA/DHCP is not subject to external attacks
Suggestions:
Define RA/DHCP options to convey URI Templates
These options, when available, take precedence over DDR
LAN
CPE
ISP
H
Do53
Server
DoT
Server
DoH
Server
(2) An administrator configures the following DNS policy:
All Hostsmalware filtering
(1) Receives a list of supported DoH services (e.g., malware filtering, no-filtering)
(3) Communicates the “malware filtering” DoH server using DHCP URI option
H
Sample Customized DHCP Configuration

## Slide 8: Issue: No @List is Returned
If the client receives a Do53 @List and an ADN, should the client use that list to resolve the ADN or should that list be assumed as locators to reach encrypted DNS servers?
Suggestion:
Recommend to always return a list of encrypted DNS @es, unless Do53 and encrypted DNS terminate on the same @es
Motivation:
Optimize the message size

## Slide 9: Next Steps
Implement the outcome of the discussion
Edits and clarification to take into account Michael and Yan’s comments
  https://github.com/ietf-wg-add/draft-ietf-add-dnr/issues/
Please review and share comments

## Slide 10: Backup

## Slide 11: DNR Design Assumptions
One or more encrypted DNS servers can be advertised by a network, e.g., DoT+DoQ+DoH
The same or distinct Authentication Domain Names may be used for DoT, DoH, DoQ, etc.
Available encrypted DNS servers may run on the same or distinct IP addresses
An encrypted DNS service (e.g., DoT, DoQ) may use a non default port number

## Slide 12: Typical Communication Flow
Clients ask for one or more encrypted DNS (e.g., DoT, DoH) by setting dedicated flags in the options
  A client that is interested in any encrypted DNS will set all the flags
Servers reply with ADN(s), a list of IP addresses, and a port number, if the requested encrypted DNS is supported
  It is RECOMMENDED to return both an ADN + a list of IP addresses
  One or more encrypted DNS types may be returned
  These services may be bound to the same or distinct IP addresses
  Alternate port numbers can be returned when default port number are not in use
  If a list of IP addresses is returned, that list is ordered
  Some recommendations to optimize the message size are included

## Slide 13: Sync DDR and DNR
DHCP servers can issue SVCB queries and cache the results
See, for example, RFC 7969
" Depending on the server capability and configuration, it may cache resolved responses for a specific period of time, repeat queries every time, or even keep the response until reconfiguration or shutdown. For more detailed discussion, see Section 7 of [RFC7227].”