## Slide 1: DHCP and Router Advertisement Options for Encrypted DNS Discovery
https://tools.ietf.org/html/draft-btw-add-home
January 2021
M. Boucadair (Orange)
T. Reddy (McAfee)
D. Wing (Citrix)
N. Cook (Open-Xchange)
Tommy Jensen (Microsoft)

## Slide 2: Overall Approach
Rely upon existing mechanisms to distribute DNS server information: DHCP, DHCPv6, and RA
Typical communication flow
  Clients ask for one or more encrypted DNS (e.g., DoT, DoH) by setting dedicated flags in the options
  Servers reply with ADN(s), a list of IP addresses, and a port number, if the requested encrypted DNS is supported
    It is RECOMMENDED to return both an ADN + a list of IP addresses
    One or more encrypted DNS types may be returned
    These services may listen on the same or distinct IP addresses
    Alternate port numbers can be returned when default port number are not in use
    If a list of IP addresses is returned, that list is ordered
    Some recommendations to optimize the message size are included

## Slide 3: Main Changes Since IETF#108
Return a list of IP addresses instead of relying upon legacy DNS options
  This is to avoid probing
  Useful if available encrypted DNS services are not available on the same IP address(es)
Generalize the specification so that the options are not tied with a particular deployment
Clarify the relationship with DEER

## Slide 4: Question #1: URI Templates in RA/DHCP?
Why?
  Provide a customized DNS configuration within a local network
There are trade-offs
  Some issues
    Create a dependency between DHCP servers (access routers) and DoH resolvers
    May increase the size of RA/DHCP messages
  Some advantages
    Fills a void as there is no standard means to retrieve the URI information from the DoH server
    Clients can immediately use the service(s); no need for extra queries to retrieve the URIs
    Does not interfere with DNS exchanges to “customize” the available services
    It is not susceptible to external attacks
Suggestions:
Define RA/DHCP options to convey URI Templates
These options, when available, take precedence over DEER
LAN
CPE
ISP
H
Do53
Server
DoT
Server
DoH
Server
(2) An administrator configures the following DNS policy:
All Hostsmalware filtering
(1) Receives a list of supported DoH services (e.g., malware filtering, no-filtering)
(3) Communicates the “malware filtering” DoH server using DHCP URI option
H
Sample Customized DHCP Configuration

## Slide 5: Question #2: No @List is Returned
If the client receives a Do53 @List and an ADN, should the client use that list to resolve the ADN or should that list be assumed as locators of the encrypted DNS?
Suggestion:
Recommend to always return a list of @es, unless Do53 and encrypted DNS terminate on the same @es
Motivation:
Optimize the message size

## Slide 6: Next Steps
Consider adopting this document as a WG item
Questions?