## Slide 1: DHCP and Router Advertisement Options for Encrypted DNS Discovery
https://tools.ietf.org/html/draft-btw-add-home
January 2021
M. Boucadair (Orange)
T. Reddy (McAfee)
D. Wing (Citrix)
N. Cook (Open-Xchange)
Tommy Jensen (Microsoft)

## Slide 2: Overall Approach
Rely upon existing mechanisms to distribute DNS server information: DHCP, DHCPv6, and RA
Typical communication flow:
  Clients ask for one or more Encrypted DNS (e.g., DoT, DoH) by setting dedicated flags in the options
  Servers reply with ADN(s), a list of IP addresses, and a port number, if the requested encrypted DNS is supported
    RECOMMENDED to return both an ADD and a list of IP addresses
    One or more Encrypted DNS types may be returned
    These services may listen on the same or distinct IP addresses
    Alternate port numbers can be returned when default port are not in use
    If a list of IP addresses is returned, that list is ordered

## Slide 3: Main Changes Since IETF#108
A list of IP addresses instead of relying upon legacy DNS options
Generalize the specification
  Remove deployment considerations
Position the draft vs. DEER
TBC

## Slide 4: Question #1: URI Templates in RA/DHCP?
There are some trade-offs
  Some Issues
    Create a dependency between DHCP servers (access routers) and DoH resolvers
    May increase the size of RA/DHCP messages
  Some advantages
    There is no standard means to retrieve such information from the DoH server
    Clients can immediately use the service(s)
    No need for extra queries to retrieve the URIs
    Allows for customized (local) configuration
Suggestion:
Define RA/DHCP Options to convey URI Templates
These options, when available, take precedence over RESINFO/DEER
LAN
CPE
ISP
H
Do53
Server
DoT
Server
DoH
Server
An administrator configures the following DNS policies:
Cparental filtering
Elseno-filtering
(2) Receives a list of supported DoH services (e.g., parental, no-filtering)
(3) Communicates the “no-filtering” DoH server using DHCP URI option
C
(3’) Communicates the “parental filtering” DoH server using DHCP URI option
Customized DHCP Configuration

## Slide 5: Question #2: No ADN is Returned
Accomodate cases where an IP address is used as a reference identifier
Should we discuss this case?
Suggestion:
Add text to the draft to cover this case

## Slide 6: Question #3: No @List is Returned
If the client receives a Do53 @List and an ADN, should the client use that list to resolve the ADN or should that list be assumed as locators of the encrypted?
Suggestion:
Recommend to always return a list of @, unless Do53 and encrypted DNS terminate on the same @

## Slide 7: Question #

## Slide 8: Question #

## Slide 9: Next Steps
Consider adopting this document as a WG item
Questions?